## Slide 1
  Searching for Exotic Interactions by Ensemble NV Centers in Diamond
Rong, Xing
CAS Key Laboratory of Microscale Magnetic Resonance
University of Science and Technology of China (USTC)
  The Second International Conference on Axion Physics and Experiment
  (Axion 2023)

## Slide 2: OUTLINES
Background
NV center magnetometer
Search for exotic interactions based on single-NV centers
Recent experiment based on Ensemble NV centers
Outlook

## Slide 4
Probing the frontiers of particle physics
with tabletop-scale experiments
Ion trap
Nature 510, 376–380 (2014)
Phys. Rev. Lett. 081801, 1–5 (2015)
Nature 606, 479–483 (2022)
Atom EDM
Phys. Rev. Lett. 116, 1–5 (2016)
Phys. Rev. Lett. 120, 013202 (2018)
Atomic magnetometer
Sci. Adv. 7, 1–9 (2021)
Nat. Phys. 17, 1402 (2021)
Solid-state NV center
Nat. Commun. 9, 739 (2018)
D. DeMille et al., Science 357, 990–994 (2017)
Notes: Kotler, S., Akerman, N., Navon, N., Glickman, Y. & Ozeri, R. Measurement of the magnetic interaction between two bound electrons of two separate ions. Nature 510, 376–380 (2014).
Kotler, S., Ozeri, R. & Kimball, D. F. J. Constraints on Exotic Dipole-Dipole Couplings between Electrons at the Micrometer Scale. Phys. Rev. Lett. 081801, 1–5 (2015).
Sailer, T. et al. Measurement of the bound-electron g-factor difference in coupled ions. Nature 606, 479–483 (2022).
Graner, B., Chen, Y., Lindahl, E. G. & Heckel, B. R. Reduced Limit on the Permanent Electric Dipole Moment of Hg 199. Phys. Rev. Lett. 116, 1–5 (2016).
Stadnik, Y. V., Dzuba, V. A. & Flambaum, V. V. Improved Limits on Axionlike-Particle-Mediated P，T-Violating Interactions between Electrons and Nucleons from Electric Dipole Moments of Atoms and Molecule. Phys. Rev. Lett. 120, 013202 (2018).
Su, H. et al. Search for exotic spin-dependent interactions with a spin-based amplifier. Sci. Adv. 7, 1–9 (2021).

## Slide 5
SPIN CAN BE USED TO EXPOLE INTERACTIONS MEDIATED BY AXION/ ALPs
Unknown coupling strength
Effective magnetic field

## Slide 6
SPIN CAN BE USED TO EXPOLE INTERACTIONS MEDIATED BY AXION/ ALPs
Thickness of vapor cell：200 μm
Experimental investigation of interaction at force range below micrometer scale is elusive due to the size of spin sensors.
G. Raffelt, Physical Review D 86, 015001 (2012).

## Slide 7: OUTLINES
Background
NV center magnetometer
Search for exotic interactions based on single-NV centers
Recent experiment based on Ensemble NV centers
Outlook

## Slide 8
nitrogen-vacancy (NV) CENTERS
[1] J. R. Maze et al., Nature 455, 644 (2008).
[2] F. Dolde et al., Nat. Phys. 7, 459 (2011).
[3] Kucsko, Georg, et al. Nature 500, 54–58 (2013).
Point defects composed of a substitutional nitrogen fixed adjacent to a vacancy;
Exhibit spin-1 triplet electronic ground state.

## Slide 9
nitrogen-vacancy (NV) CENTERS
Quantum sensor for temperature, electric-field, stress, magnetic field, and nearby spin due to its spin properties.

## Slide 10
Principle of magnetic field sensing based on NV CENTERS
>
>

## Slide 11
Magnetic field Sensing protocol——Pulse mode
Polarization
Readout
Evolution
Laser
MW
Sequence
Interferometer principle

## Slide 12
Magnetic field Sensing protocol——CW mode
Continuously sensing
Laser
Modulated MW
Sequence
Frequency modulation to overcome flicker noise
Y. J. Xie et al. Sci. Bull. 66, 127–132 (2021).

## Slide 13
A video

## Slide 14: OUTLINES
Background
NV center magnetometer
Search for exotic interactions based on single-NV centers
Recent experiment based on Ensemble NV centers
Outlook

## Slide 15: UTILIZING SINGLE-SPIN SENSOR TO SEARCH FOR EXOTIC INTERACTIONS

## Slide 16: SEARCHING FOR ELECTRON-NUCLEON MONOPOLE-DIPOLE INTERACTION
  Nature Communications 9, 739 (2018)
The pulse sequence is designed to accumulate the possible distance-dependent effect.

## Slide 17
EXPERIMENTAL SETUP

## Slide 18
No signal
SEARCHING FOR ELECTRON-NUCLEON MONOPOLE-DIPOLE INTERACTION
  X. Rong et al., Nat. Commun. 9, 739 (2018), X. Rong et al., PRL 121, 080402 (2018),
  M. Jiao et al., PRL 127, 010501 (2021)
  A serious of work has been done.

## Slide 19: How to further improve searching sensitivity？
Achieve number enhancement directly using ensemble NV centers in one diamond.
： number of electron spins in diamond
： number of integrated chip
Develop array of diamond sensors.
——integrated on-chip sensor
Pu Huang et al. in progress
  H. Liang et al., Natl. Sci. Rev nwac262 (2022)

## Slide 20: Challenges of using ensemble NV centers
Diamond sensor
  Optimize sample concentration
  Optimize sensing volume
Poor
coherence
Poor
sensing number
concentration
Optimize concentration to achieve higher sensitivity
Optimize thickness to
achieve sub-millimeter search

## Slide 21: OUTLINES
Background
NV center magnetometer
Search for exotic interactions based on single-NV centers
Recent experiment based on ensemble NV centers
Outlook

## Slide 22: Experiment based on Ensemble NV
We developed a 23 μm thick 12C,14N-enriched layer on an electronic-grade diamond as our layer sensor.
NV concentration layer sensor：14 ppm
Exhibit excellent coherence properties.
Home built diamond sensor
Notes: 23 μm 12C ,14N enriched layer on an electronic-grade diamond

## Slide 23: Searching for exotic spin interactions by ensemble-NV-diamond magnetometer
  H, Liang, NSR 2022, D. Wu et al., PRL accepted (2023)

## Slide 24
Experiment scheme of searching for
The exotic Velocity-dependent interaction
Two thin layers of nitrogen-vacancy (NV) ensembles in two individual diamonds are implemented as the spin sensor and the spin source, and are initialized by 532 nm laser from the side and top, respectively.
We independently manipulate the spin states of the spin sensor and the spin source by applying microwaves of two distinct frequencies.
A 94 G static magnetic field B0 was applied along the NV symmetry axis of the spin sensor to separate |ms = ±1⟩ spin states
v
Notes: The ensemble resonance line shape is broadened by both the distribution of linecenters (left) and the distribution of linewidths (right) of the constituentspins.

## Slide 25: Experiment Setup based on Ensemble-NV-diamonds
Schematic of the experimental configuration
Photo of part of the setup
NV Ensemble Magnetometer
Notes: 23 μm 12C ,14N enriched layer on an electronic-grade diamond

## Slide 26: Performance of NV ensemble magnetometer
Coefficient of the magnetic field to the output of the magnetometer was determined by the max slope of the CW spectrum.
The magnetic measurement capacity was demonstrated using a calibration signal generated by a coil.
Sensitivity：2 nT/Hz1/2 from 1 to 2 kHz

## Slide 27: Measurement of the polarized spin density
The polarization of the spin source was modulated by periodically switching MW II via a microwave switch with
The polarized spin density when MW II was on-resonance.
First, the polarized spin density of spin source is obtained by measuring the magnetic dipole-dipole interaction between the two NV ensembles.

## Slide 28
The spin source was modulated by a piezoelectric bender to vibrate with a frequency = 1.337 kHz.
exotic velocity-dependent signal in-phase channel
other displacement-dependent signals quadrature channel
Experimental searching for
The Velocity-dependent interaction

## Slide 29
With 26-hour data, the first order amplitude of effective magnetic field pT with the reduced chi-square .
For λ=1 mm, .
The statistical errors can be further reduced by improving the stability of our system and realizing longer measurement.
The systematic errors mainly come from the uncertainties of geometric parameters of the spin source.
Statistical errors and systematic errors

## Slide 30: New constraints on and
V14: new constraints for the force range km
V6: new constraints for the force range cm
Manuscript preparing

## Slide 31: SUMMARY
NV center is a powerful platform for investigating exotic spin dependent interactions.
In the future, other types of spin source can be incorporated to investigate new physics with NV center in diamond.

## Slide 32: ACNOWLEDGEMENTS
Man Jiao
Diguang Wu
Jiangfeng Du
Hang Liang
Yue Huang
Runqi Kang
Yi-Fu Cai
Ya Wang