## Slide 1
Polarized HD target
for SPring-8 LEPS experiment
Norihito Muramatsu (IMP, CAS)
PBT2026 Mar 30 – Apr 2, 2026
D
H
Hadron photoproduction experiment in Japan

## Slide 2
History of the HD target
A solid hydrogen-deuteride target with proton or/and deuteron polarization.
Merit: HD molecule does not contain heavy nuclei such as C & N.
1970s-1980s 1995-2000 ~2000 2005-2020
Syracuse BNL (for LEGS) Orsay (for Graal) RCNP (for LEPS)
A. Honig et al. A.M. Sandorfi et al. J.-P. Didelez et al. H. Kohri et al.
Many materials come from Prof. Hideki Kohri (RCNP, Osaka Univ.).
I joined only at the beginning of this project.
Introduction (Polarization mechanism, Physics motivation)
Target production system (Various cryostats & Magnets)
Experimental results (Distillation, NMR, Proton polarization test)
1 / 14
Outline of this talk
Unfortunately, this project was not completed.

## Slide 3
Introduction (Polarization mechanism, Physics motivation)
Target production system (Various cryostats & Magnets)
Experimental results (Distillation, NMR, Proton polarization test)

## Slide 4
What is the polarized HD target?
Boltzmann distribution
: Boltzmann constant
: Proton magnetic moment
: Magnetic field
: Temperature
Temperature (mK)
Polarization (%) at 17 T
H polarization
D polarization
E
Ｂ
E+
E-
N
Proton polarization
In case of B = 17 Tesla & T = 10 mK, P ~ 90%
 Static polarization method
(“brute force”)
2 / 14

## Slide 5
What is the polarized HD target?
Polarization is frozen for a long time (~1 year)
even with a lower B-field & a higher temperature.
(For D2, the roles of ortho and para are reversed due to Bose statistics.)
😓 It is not practical to keep 17 T & 10 mK during the experiment…
2-3 months
ageing
0.01%
3 / 14

## Slide 6
Physics motivations
4 / 14
Strangeness content in the proton
Beam-target asymmetry in  photoproduction. [PRC 58 (1998) 2429]
Double polarization observables in baryon resonance spectroscopy
Pseudoscalar meson photoproduction is described by only four complex
amplitudes. Measurement of the polarization observables in addition to
the cross section are helpful to completely solve those amplitudes.
-channel Pomeron exchange
-knockout
1%
0.25%
Relative phases of
to the
-channel exchange

## Slide 7
Introduction (Polarization mechanism, Physics motivation)
Target production system (Various cryostats & Magnets)
Experimental results (Distillation, NMR, Proton polarization test)

## Slide 8
Original concept of the target operation
125 km
DRS: Dilution Refrigerator System
TC : Transfer Cryostat (1 & 2)
SC : Storage Cryostat
IBC : In-Beam Cryostat
Finally, the project has finished
at this stage because of the world
helium crisis, etc.
5 / 14

## Slide 9
Dilution refrigerator
Leiden Cryogenics DRS-2500
Cooling power : 2500μW at 120 mK
Lowest temperature : 6 mK
HD target cell
Kle-F container
(p-free for NMR)
Narrow Al wires
(20% in weight)
2.5 cm
3He/4He mixing chamber to cool down the cold finger.
Inner thread is used when taking out the cell by a TC.
6 / 14

## Slide 10
Superconducting magnet
Y axis
DRS
Magnet
Magnetic Field : 17 Tesla
Homogeneity of Magnetic Field : 5×10-4 for 15 cm
Magnetic Field (Tesla)
Y Position (mm)
HD
target
The HD production system is
embedded under ground.
The cell can be taken
out from the top part.
7 / 14

## Slide 11
Transfer cryostats & Storage cryostat
Both are 4He cryostats & provided from the Orsay group.
Magnetic Field : 2.5 Tesla
Temperature : T~1.5 K
Homogeneity : 10 -4
for target region
Magnetic Field : ~0.2 Tesla
Temperature : T ~ 4.2 K
TC for DRS
TC for IBC
SC
8 / 14

## Slide 12
In-beam cryostat
Cell insertion
by TC
Target polarization can be changed to the longitudinal or transverse directions by coils.
Many polarization observables can be obtained by combining with the circular or linear polarization of γ-ray beam.
T=300 mK
B=1 T
9 / 14

## Slide 13
Introduction (Polarization mechanism, Physics motivation)
Target production system (Various cryostats & Magnets)
Experimental results (Distillation, NMR, Proton polarization test)

## Slide 14
HD gas distillation
T~18 K
T~20 K
T~21 K
0
H2 solid
H2 liquid
H2 gas
Refrigerator
Heater
Filled by Heli-packs
HD solid
HD liquid
HD gas
Gas chromatograph
(T~110 K)
Quadrupole
Mass
Spectrometer
T. Ohta et al. NIM A 640 (2011) 241
10 / 14

## Slide 15
Mass/Charge (u/e)
Elapsed Time in Gas Chromatograph (min)
Partial Pressure (mbar)
o-H2
p-H2
HD
D2
HD gas distillation
H2 concentration (p-H2 + o-H2) during gas distillation
HD purity
~99.99%
T. Ohta et al. NIM A 664 (2012) 347
Commercial-base HD gas purity before distillation is about 95%.
 The new distillation system has enough ability to purify an HD gas.
(The amount of o-H2 is also adjustable.)
11 / 14

## Slide 16
NMR measurement
Conventional NMR system (~80 kg)
Portable NMR system (~7 kg)
The polarization should be measured at any place during the target transportation
from RCNP to SPring-8. Need a system which is easy to move.
 Portable NMR measurement system by PCI eXtensions for Instrumentation
(PXI) with a LabVIEW control.
T. Ohta et al. NIM A 633 (2011) 46
12 / 14

## Slide 17
Proton polarization test
Relaxation of the H polarization
T1 = 8  2 months
T. Ohta et al., Review of Scientific Instruments 91, 095104 (2020)
Thermal Equilibrium ~2000 times larger
at 4.2 K and 0.87 T PH = 44  1 %
3-month ageing was performed with DRS under B=17 T & T=30 mK.
13 / 14

## Slide 18
Summary
14 / 14
HD polarized target (90% for H and 60% for D) is producible by “brute force” under a high magnetic field (17 T) & a vary low temperature (10 mK). It is useful to reduce heavy element contamination.
After an HD distillation down to the H2 contamination of 0.01% and a 3-month ageing process, it has been confirmed that the relaxation time can be the order of a year.
So far, only the proton polarization has been done. But the deuteron polarization should also be available with adiabatic fast passage and can be frozen by the contamination of o-D2. The polarization of H or/and D is controllable.

## Slide 19
Collaboration list in 2005